## Slide 1: Slope stability at Lot 12
Site investigation findings and recommendations
R. Kalatehjari, GEOTECH-LAB | 3 October 2026

## Slide 2: Background

## Slide 3: Site and geology
Residual soils over weathered greywacke
  Silty clay to 3 m, then clayey silt
Groundwater at 2.5 m below ground level
Existing timber wall shows signs of rotation
Lot 12 retaining wall — client briefing
3
Notes: Mention the site walkover on 12 August and the photos in Appendix A.

## Slide 4: Investigation scope
Three boreholes to 8 m
Six CPTs
Laboratory testing: Atterberg limits, triaxial
Lot 12 retaining wall — client briefing
4

## Slide 5: Results

## Slide 6: Effective stress paths
Effective stress paths for BH1 samples
Lot 12 retaining wall — client briefing
6

## Slide 7: Strength parameters
Sample | Depth (m) | c' (kPa) | φ' (°)
BH1-S1 | 1.5 | 12.3 | 31.5
BH1-S2 | 3.0 | 8.7 | 33.0
BH2-S1 | 2.0 | 15.1 | 29.8
Lot 12 retaining wall — client briefing
7

## Slide 8: Factor of safety
Both cases are below the 1.5 target for permanent works.
Chart: Factor of safety
| Static | Seismic
FoS | 1.32 | 1.08
Target | 1.5 | 1.2
Lot 12 retaining wall — client briefing
8

## Slide 9: Comparison
Option A: deeper embedment
Option B: soil nails
Option C: rebuild as gravity wall
Plan view
Lot 12 retaining wall — client briefing
9

## Slide 10: Recommendation
Increase wall embedment by 2 m and add drainage behind the wall.
Lot 12 retaining wall — client briefing
10

## Slide 11: Questions?
Lot 12 retaining wall — client briefing
11